Procedure to install and configure Loreta/sLoreta for the use in/with HBIdb or WinEEG:

Preamble:

A few recommendations how to use WinEEG with Loreta and sLoreta:

(A) We do not recommend to install WinEEG/Loreta/sLoreta in Program Files, because changes in this folder are automatically blocked by OS and it may lead to some issues.

(B) The default installation path of both, Loreta and sLoreta, respectively, however IS within the Program Files folder. Therefore (and although we recommend to not install within the Program Files folder) the following description of the procedure to install and configure Loreta/sLoreta is assuming the software to be installed at its default path \program files (x86).

(C) WinEEG generates file for sLoreta here: \Mitsar\WinEEG\Temp\WinEEGLoretaVoltage.txt

If you are missing it, please, check sLoreta settings and change for proper location.

Procedure:

(1) Install Loreta.

(2) Start either HBIdb or WinEEG

When you attempt (within HBIdb or WinEEG) to open Loreta for the first time, you will be asked for the place where "loreta.exe" is located. To tell HBIdb/WinEEG where it can find Loreta, proceed as follows:

(3) Open an EEG-file (for this procedure, it doesn't matter which EEG-file):

(4) Go to "Analysis" and select "Source distribution (LORETA)"

(5) HBIdb or WinEEG will ask for the place where "loreta.exe" is located

So, navigate to: 
C:\Program Files (x86)\LORETA\020-Main
which is the default path where Loreta installs the software.

(6) Double-click loreta.exe and you are done :-)

Now we want to configure sLoreta:

(7) Install sLoreta

(8) Download and extract the "Matrix" folder:

http://www.hbimed.com/fileadmin/user_upload/images_and_pdfs/support/downloads/sLoreta_Matrix/Matrix.zip

(9) Copy the whole "Matrix" folder or just its contents (the two "coordinates..." files) into the sLoreta folder C:\Program Files (x86)\sLORETA:

At the end of this step it is important that the sLoreta folder has a "Matrix" folder, which contains the two files "coordinates_19.spinv" and "coordinates_19.sxyz".

(10) Start sLoreta and open "Viewer/Explorer"

(11) In the "Viewer/Explorer" window go to menu "File" and click to "Open electrode coordinates file":

(12) Select "coordinates_19.sxyz" (in the Matrix folder we just created).

(13) Go to menu "File" and click to "Open transformation matrix file":

(14) Select "coordinates_19.spinv" (in the Matrix folder we just created).

(15) Go to menu "File" and click to "Open EEG/ERP file"

(16) First, a window will open to "Define sampling rate (Hz)". Enter "250" and click "OK".

(17) Thereafter a second window (a file dialog box) will appear to locate the "WinEEGLoretaVoltage.txt" file. Navigate to the Loreta folder (C:\Program Files (x86)\LORETA) and select file "WinEEGLoretaVoltage.txt". Alternatively, the file might be at \Mitsar\WinEEG\Temp\WinEEGLoretaVoltage.txt.

(18) Go to menu "jobs". Don't worry when the "Recent jobs" window will not show any of the set parameters and file locations. Click to "SaveCurrent". Thereafter, the window will show the set values and paths.

To use sLoreta from now on just load the software, open viewer/explorer, goto Jobs and press "Load Selected"

This will then load the previously created file from Loreta.